## Slide 1: Binoculars (& Binoviewers)
Ken Anderson
FAAC 3/19/2016

## Slide 2: Binoculars
Why Binoculars
  Natural two eye viewing (Sqrt 2 signal to noise brain multiplier) - Twice the aperture of monocular
  Wider true field of views than telescopes
  Smaller/More portable than larger telescopes
  Small ones are hand holdable
    Often 7x50 recommended
    My limit is 9x63 and 15x63 Orion Mini Giants (2.3lbs each), but monopod preferred for these higher powers.
  Cost – Low Cost of Entry for small binoculars

## Slide 3: Types of Binoculars
Porro –Straight through, smaller
Roof Mounted – standard (BAK-4 and BK7 both good coatings)
Zoom – Not recommended (narrower FOV)
Image stabilized – hand hold stabilization of moderate aperture and higher power but very costly

## Slide 4: Binocular Specification
Magnification x Aperture (mm) = Visibility Factor
  Magnification = Power
    Lower magnification yields wider area of sky
      Advantage of hand holdability at 10x and below
    Higher magnification yields greater detail but less sky
  Aperture = Light Gathering & Luminance
    Smaller is hand holdable but has darker skies, less stars/DSOs
      ~7x50 most common (7mm exit pupil)
    Larger may require monopod/tripod but has brighter skies, more stars/DSOs
      50mm (or 63mm mini giants( typical limit of hand holdability)

## Slide 5: Ultra Wide Low Power Gallileans (Constellation Viewing – entire constellations!)
Kasai/Blue Planet Optics 2.3x40mm 28 deg AFOV
  Very low eye relief & small eyepiece opening (not for eyeglass wearers!) – the closer you can get your eye the wider the view.
  Optional filter holders & hands free headset
  Vixen 2.1x42mm
    Very low eye relief & larger eyepiece opening (easier daytime/meteor shower viewing) – the closer you can get your eye the wider the view.
  What can you see?
    Pan Milkyway
    Able to Pleadies and Hyades in same view
    Able to see Orion’s belt and sword in same view
    M32 lo0ks like sky chart with guide stars
    Often multiple planets in same view
    Great for fireworks, sporting events, theater/concerts, kid events!!!!

## Slide 6: Vixen Ascott 10x50 SW
10x50 8.5 deg AFOV
  5mm exit pupil
  Lenses and mirrors to get wide view
  Hand holdable (but less shake and able to see more detail when on monopod)
  Able to lay down or sit in zero gravity lawn chair and look at zenith!
What can you see?
Entire Hyades!
  Pleadies or Beehive Star Clusters look good.
  Belt of Orion
  Sword of Orion with M42 visible
  Multiple DSOs in same view (M81/M82, comets, planets)

## Slide 7: Orion Mini-Giants & Garrett Pistol Grip Monopod (limit of hand holdability)
9x63 5.0 deg AFOV
  7mm exit pupil, 20mm eye relief
  Only 2.3 lbs.
  Hand holdable (but less shake and able to see more detail when on monopod)
  15x63 3.7 deg AFOV
    4.5mm exit pupil, 29mm eye relief
  Only 2.3 lbs.
  Marginably holdable (much less shake and able to see much more detail when on monopod!)
Able to lay down or sit in zero gravity lawn chair and look at zenith!
What can you see?
  Pleadies or Beehive Star Clusters look great!
  Sword of Orion with M42 visible
  M81.M82 in same view
  Multiple DSOs in same view (M81/M82, comets, planets)

## Slide 8: Large Binoculars
Why Large Binoculars
  Natural two eye viewing (Sqrt 2 signal to noise brain multiplier) - Twice the aperture of monocular
  Large aperture enables you to see more and dimmer DSOs with greater detail.
  Wider true field of views than telescopes, but not as wide as smaller binoculars
  Smaller/More portable than larger telescopes, but not as portable as small hand holdable binos
Disadvantage – 70mm+ require tripods (extra setup/weight)
    Straight through limited to 70 deg azimuth (neck limit) but easy to aim
    45/90 deg able to see zenith (90 deg azimuth) but harder to aim. Plus able to swap eyepieces (power, AFOV/TFOV)
What can you see?
  M31 (two FOV from dark site Mauna Kea – best view of M31 ever)
  Pleadies or Beehive Star Clusters look awsome (especially when planet or moon passes through!
  Sword of Orion with M42 visiblelooks awsome!
  M81.M82 in same view
  Multiple DSOs in same view (M81/M82, comets, planets)
  Sun Spots with great detail (white light solar filter needed)

## Slide 9: 25x100mm Appogee Straight Through Binos
Straight through limited to 70 deg azimuth (neck limit) but easy to aim
Fixed Eyepiece power 25x and 3.5deg TFOV (cloudy nights says less)
Inexpensive/Light Weight camera tripod (cloudy nights recommends heavier/stiller/taller more expensive tripod for stability and less vibration
  Not able to point to zenith, and no space for head/neck space to do so (but neck limited to 70 deg anyway).
  More difficult to mount bino on tripod (than Versa Go mount L bracket)

## Slide 10: FAAC Orion 100mm Right Angle Binos
FAAC Orion 100mm Right Angle Binos
  90 deg able to see zenith (90 deg azimuth) plus able to swap eyepieces (power, AFOV/TFOV)
    22x Orion straight barrel – came w/ binos – able to tighten w/o issue (used w/ public)
    24mm 68 AFOV TV Panoptic (widest view) – indented barrel (personal, previous FAAC member got indented barrel stuck!)
    20mm, 15mm, & 9mm 66 AFOV Orion Expanse indented barrel
  Orion Vixen Versa Go Alt Azimuth Mount
    Able to point to zenith and offset angle allow head/neck space to do so
    L bracket easy to install on upside down binos
    L bracket/bino east to install on Versa Go mount
  Effective Aperture a little above 80mm (ref cloudy nights)
  Red dot finder recommended to assist in aiming

## Slide 11: Denk II Binoviewers
Advantages
  Able to use two eyes with your telescope!
    More natural two eye viewing with SQRT 2 signal to noise multiplier
  More Detail on brighter DSOs and planets, or Moon.
  Power switches and OCSs enable multiples powers and FOV with single pair of eyepieces (no need to buy multiple pairs of eyepieces!)
Disadvantage
  Half the aperture per eye (may not see dimmer DSOs)
  Narrower TFOV than original telescope (& pure binoculars)
  Some people have issues merging images in both eyes (therefore try before buy)

## Slide 12: Denkmeier LOA 21 3D eyepieces
3D viewing in binoviewers or 45/90 deg binos that accept removable eyepieces
One eyepiece has 5 square arrays (center, up down, left, right) plus nominal for 6 distinct depths. Indentations on that eyepiece can place center array either at closest or furthest appeared distances.
Artificial 3D depth for DSOs and background stars (no correlation to real distances)
Option to buy 3rd 2D eyepiece for planets, moon, sun (doubt anyone would want to look at DSOs in 2D when 3D is available)
P.S. Denk will soon be offering 3D hand held binos for Milkyway, Small Constellations, Hyades, Perseus A, M45, M44, M31, M42, M8, M13, etc.

## Slide 13: Questions & Answers